## Slide 1: What is Microwave
Microwave Communications
  Is simply a high radio frequency link specifically designed to provide signal connection between two specific points.
  Also coined as Line-of-Sight or LOS communications, Radio Link, Point-to-Point communications.

## Slide 2: What is Microwave Communication
A communication system that utilizes the radio frequency band spanning 2 to 60 GHz. As per IEEE, electromagnetic waves between 30 and 300 GHz are called millimeter waves (MMW) instead of microwaves as their wavelengths are about 1 to 10mm.
Small capacity systems generally employ the frequencies less than 3 GHz while medium and large capacity systems utilize frequencies ranging from 3 to 15 GHz. Frequencies > 15 GHz are essentially used for short-haul transmission.
2

## Slide 3: Classification of Microwave
Nature
  Analog
  Digital
Distance / Frequency
  Short Haul
    used for short distance microwave transmission usually at lower capacity ranging from 64 kbps up to 2Mbps
  Medium Haul
  Long Haul
    used for long distance/multi-hop microwave transmission. Used for backbone route applications at 34 Mbps to 620 Mbps capacity
Capacity / Bandwidth
  Light (Narrow Band)
  Medium (Narrow Band)
  Large (Wide Band)

## Slide 4: Advantages of Microwave System
The gain of an antenna is proportional to its electrical size.
A 1% bandwidth provides more frequency range at microwave frequencies than that of HF.
Microwave signals travel predominantly by LOS.
There is much less background noise at microwave frequencies than at RF.
Microwave systems do not require a right-of-way acquisition between stations.
Fewer repeaters are necessary for amplification.
Underground facilities are minimized.
Increased reliability and less maintenance.

## Slide 5: Disadvantage of Microwave System
More difficult to analyze electronic circuits
Conventional components (resistors, inductors, and capacitors) cannot be used at microwave frequencies.
There are physical limitations in creating resonant circuits at microwave frequencies.
Conventional semi-conductor devices do not work properly at microwave frequencies because of
  Inherent inductances and capacitances of the terminal leads and
  Transit time
For amplification, vacuum tubes are used such as klystrons, magnetrons and traveling wave tubes (TWT).
Distance of operation is limited by line of sight (LOS).
Microwave signals are easily reflected and/or diverted because of the very short wavelength.
Atmospheric conditions such as rain/fog can attenuate and absorb the microwave signal especially at 20 GHz and up.

## Slide 6: Terrestrial Microwave
Types Of Microwave Stations
  Terminals – are points in the system where the baseband signals either originate or terminate
  Repeaters – are points in the system where the baseband signals maybe reconfigured or simply repeated or amplified.
    Passive Microwave repeaters – a device that re-radiates microwave energy without additional electronic power.
      back to back
      billboard type
    Active Microwave repeater – a receiver and a transmitter placed back to back or in tandem with the system. It receives the signal, amplifies and reshapes it, then retransmits the signal to the next station.