## Slide 1: Memory Classification

## Slide 2: Semiconductor Memory Types
Random Access Memory (RAM)
Read Only Memory (ROM)
Programmable Read Only Memory (PROM)
Eraseable Programmable Read Only Memory (EPROM)
Electronically Eraseable Programmable Read Only Memory (EEPROM)
Flash Memory

## Slide 3: Random Access Memory
RAM allows reading and writing (electrically) of data at the byte level
Two types
  Static RAM
  Dynamic RAM
Volatile

## Slide 4: Read Only Memory (ROM)
Sometimes can be erased for reprogramming, but might have odd requirements such as UV light or erasure only at the block level
Sometimes require special device to program, i.e., processor can only read, not write
Types
  EPROM
  EEPROM
  Custom Masked ROM
  OTPROM
  FLASH

## Slide 5: ROM Uses
Permanent storage – nonvolatile
Microprogramming
Library subroutines
Systems programs (BIOS)
Function tables
Embedded system code

## Slide 6: EPROM
Written to only with a programmer.
Erased with ultraviolet light
Positive
  non-volatile storage without battery
  can write to it, but only with aid of programmer
Negative
  programmer requirements
  Expensive
  locations must be erased before writing

## Slide 7: EEPROM
Written to with either programmer or the processor (electrically)
Erased with either a programmer or the processor (byte-by-byte electrically)
Positive
  non-volatile memory without batteries
  programmable a single-location at a time
Negative
  Expensive
  only smaller sizes available
  extremely slow write times (10 mS vs. 100 to 200 nS)

## Slide 8: Custom masked ROM
You send the ROM manufacturer your data and they mask it directly to the ROM
Use only when you are selling large volume of a single product
Positive
  becomes cheaper to use for approximately more than 2000 parts
  components come from chip manufacturer already programmed and tested taking out a manufacturing step
Negative
  costs several thousand dollars for custom mask
  software changes are costly
  cannot be reprogrammed

## Slide 9: OTPROM
Uses fuses that are burned to disconnect a logic 1 and turn it to a logic 0.
Written to by you using a programmer similar to EPROM
Once it's written to, the data is in there forever.
Positive
  cheaper than EPROM due to cheaper packaging
  more packaging options than EPROM due to less constraints like erasure window
  standard "off-the-shelf" component
  cheaper than Custom masked ROM up to about 10,000 devices
Negative – to reprogram, have to throw out the chip - Should only be used for stable design

## Slide 10: FLASH
These memories are basically EEPROMs except that erasure occurs at the block level in order to speed up the write process
Non-volatile
This makes FLASH work like a fast, solid state hard drive
Positive
  non-volatile
  higher densities than both SRAM and DRAM
Negative
  process of storing data is at a block level (and slower)
  data cell must be erased before writing data to it

## Slide 11: DRAM Operation
Address line active when bit read or written
Logic ‘1’ closes transistor switch (i.e., current flows)
Write
  Voltage to bit line – High for 1 low for 0
  Signal address line – Controls transfer of charge to capacitor
Read
  Address line selected – transistor turns on
  Charge from capacitor fed via bit line to sense amplifier
  Compares with reference value to determine 0 or 1

## Slide 12: Static RAM (SRAM)
Essentially uses latches to store charge (transistor circuit)
As long as power is present, transistors do not lose charge (no refresh)
Very fast (no sense circuitry to drive nor charge depletion)
Can be battery-backed – A small battery is piggy-backed to the RAM chip an allows data to remain even when power is removed (Not possible with DRAM)
More complex construction
Larger per bit
More expensive
Used for Cache RAM because of speed and no need for large volume or high density

## Slide 39
Fig: Timing Diagram for STA 8000.
For the timing diagram for LDA all are memory read.